### Test Report of Hi-Pot

- Test Purpose：

Between contacts and shielded, the puncture voltage must not less than 1.5 KV (r.m.s.), all the leakage current must no greater than 0.5 mA for 1 minute.

- Test condition：

  - Test date：28-May-2013

  - Part number：AJ-069SH-8-F-R4-B4-N4

  - Test sample Size：5pcs.

  - Test position：Contact pins, shielded.

  - Test equipment：Puncture Voltage<0-5KV AC>Leakage current ：0.5~10 mA.

  - Manufacturer：GW；Model：GPI-5005T.(as photo 1)

【Photo 1】

- Test Method：

The samples were tested as specified in EIA-364-20B, without breakdown or any current leakage greater than 0.5 mA.

A. At 1.5KV rms for one minute between shield and contacts.

- Result：

As table 1 and attachment A.

Table 1   Test result

| Item Sample | Shield to contacts |
| --- | --- |
|  | Appearance | Value |
| All | OK | Passed |

※Judgment: ( Accept □ Reject

Approver：Jason  2013/05/28     Tester：Eva  2013/05/28

P.1 of 2

Attachment A.

| Sample No. | Shield to contacts |
| --- | --- |
| 01 |  |
| 02 |  |
| 03 |  |
| 04 |  |
| 05 |  |

P.2 of 2